## Slide 1: تمرین سری اول
تحویل تمرین سری 1 | 9 اسفند | 5
تحویل تمرین سری 2 | 23 اسفند | 7
تحویل تمرین سری 3 | 21 فروردین | 9
میان ترم | 23 فروردین | -
تحویل تمرین سری 4 | 4 اردیبهشت | 11
تحویل تمرین سری 5 | 18 اردیبهشت | 13
تحویل تمرین سری 6 | 1 خرداد | 15
هفته
تاریخ (دوشنبه 11 تا 13)

## Slide 2: تمرین ها
  \\fileserver\common\szamani\Design Automation (BS)\homework and project\
  دوشنبه‌ها ساعت 11 تا 13
  آزمایشگاه طراحی خودکار سیستم های دیجیتال

## Slide 3: زبان توصیف سخت‌افزار
Hardware Description Language

## Slide 4: زبان‌ها
  VHDL
    یادگیری حداقل یک زبان به طور کامل
      یادگیری ناقص و سعی و خطا  سخت شدن توصیف و اشکال‌زدایی
    اصول یکسان – ساختارهای نحوی متفاوت
    VHSIC HDL (اوایل دهة 1980)
    مبتنی بر زبان ADA

## Slide 5: VHDL
کاربردها:
  مستندسازی:
    به جای توصیف زبان طبیعی:
      نادقیق (برداشت‌های مختلف)
      غیر قابل پردازش

## Slide 6: VHDL
کاربردها:
  مدل‌سازی:
    مراحل اولیة طراحی:
      عملکرد و رفتار کلی مشخص است
      توصیف الگوریتم با دستورهای رفتاری
      کمک به فهم صورت مسأله
      جلوگیری از سرایت اشکالات به سطوح پایین طراحی

## Slide 7: VHDL
کاربردها:
  مدل‌سازی:
    مثال: کنترل‌کنندة آسانسور
...
while (true) loop
begin
...
if (REQUEST = true)then
if (REQUEST_FLOOR > CURRENT_FLOOR) then
MOVE_UP (CURRENT_FLOOR, ...);
else
MOVE_DOWN (CURRENT_FLOOR, ...);
end if;
end if;
...
end loop;
...

## Slide 8: VHDL
کاربردها:
  سنتز
    تولید خودکار مدار از توصیف
    زیرمجموعة قابل سنتز
      لزوم آشنایی با این زیرمجموعه
      تفاوت ابزارها  portable code
        کد غیر قابل سنتز برای دیگری
        مدار متفاوت
      کلیات یکسان
    این درس:
      موارد کلی مشترک
      نحوة کدنویسی مناسب

## Slide 9: VHDL
کاربردها:
  درستی‌سنجی
    محیط درستی‌سنجی: testbench
    عناصر اصلی:
      طرح مورد آزمون
      تولید و اِعمال بردارهای ورودی
      مشاهده و تحلیل خروجی‌ها

## Slide 10: VHDL
کاربردها:
  درستی‌سنجی
    تولید بردارهای ورودی:
      تصادفی
      انتخاب هوشمندانه
      الگوریتم‌های تولید خودکار بردارهای آزمون (ATPG)
    نیاز به توصیف با کد VHDL
      برنامه‌نویسی روالی
      خواندن از فایل

## Slide 11: VHDL
  مثال:
    سخت‌افزار محاسبة (x2 + y2)1/2
    مقایسه با نتیجة رفتاری
architecture TBENCH of ENT_BENCH is
procedure WAVE_GEN (signal X:out integer, signal Y:out integer)
variable I integer:= 0;
begin
for VX in 0 to 63 loop
for VY in 0 to 63 loop
begin
X <= VX after I*10 ns;
Y <= VY after I*10 ns;
I:= I + 1;
end loop;
end procedure WAVE_GEN;
begin
WAVE_GEN (X, Y);
L1:L_MODULE port map(X,Y,L);
L_BEHAVE <= (X**2 + Y**2)**0.5;
ERROR_SIG <= L_BEHAVE xor L;
end architecture TBENCH;

## Slide 12: سطوح تجرید (Levels of Abstraction)
رفتاری:
    توصیف عملکرد مطلوب (الگوریتمی)
    بدون پرداختن به مدار
    همة امکانات VHDL
    قابل نمایش با روندنما (flow chart)

## Slide 13: سطوح تجرید

## Slide 14: سطوح تجرید
انتقال ثبات (Register-Transfer Level) RTL:
  مسیر داده
    ثبات‌ها
    مدارهای ترکیبی
    منابع ارتباط دهنده‌ بین آنها
      گذرگاه
      مالتی‌پلکسر
      سیم
      ...
  کنترل‌کننده (مسیر کنترل)
    ماشین حالت متناهی FSM

## Slide 15: سطوح تجرید
انتقال ثبات:
process (CLK)
begin
if (CLK’event and CLK = ’1’) then
Z <= D;
end if;
end process;
process (A, B, M)
begin
if (M = '1‘) then
D <= A * B;
else
D <= A – B;
end if;
end process;

## Slide 16: سطوح تجرید
گیت:
architecture GATE_LEVEL of ADDER is …. begin L1:XORG port map(X1, Y1, T1); L2:ANDG port map(X1, Y1, T2); L3:XORG port map(T1, Z, S1); L4:ANDG port map(T1, Z, T3);
L5:ORG port map(T3, T2, C1);
….
end GATE_LEVEL;

## Slide 17: توصیف سخت‌افزار با VHDL
جزئیات:
  Language Reference Manual
    به عنوان مرجع اصلی
    1076 LRM Ieee Standard Vhdl Language Reference Manual.pdf
  زيرمجموعة قابل سنتز: استاندارد 1076.6
  VHDL-AMS 1076.1
    فقط شبیه‌سازی
    نحوة شبیه‌سازی: معادلات دیفرانسیل

## Slide 18: VHDL Structural Elements
Entity: Interface
Architecture: Implementation, behavior
Configuration: Structure, hierarchy
Process: Sequential Execution
Package: Components (Modular design), Utilities (data types, constants, subprograms)
Library: Group of compiled units, object code

## Slide 19: Entity
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
Interface description
No behavior/implementation definition
entity ADDER is port( A, B: in integer range 15 downto 0; SUM: out integer range 15 downto 0; CARRY: out bit ); end ADDER;
Linking via port signals
  data types
  signal width
  signal direction
in bit_vector (3 downto 0); out bit_vector (3 downto 0);

## Slide 20: Architecture
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end HALFADDER; architecture RTL of HALFADDER is begin SUM <= A xor B; CARRY <= A and B; end architecture RTL;
Implementation of the design
Always connected with a specific entity
  one entity can have several architectures
  entity ports are available as signals within the architecture
Contains concurrent statements

## Slide 21: Architecture Structure
architecture RTL of STRUCTURE is subtype DIGIT is integer range 0 to 9; constant BASE: integer := 10; signal DIGIT_A, DIGIT_B: DIGIT; signal CARRY: DIGIT;
begin DIGIT_A <= 3; SUM <= DIGIT_A + DIGIT_B; DIGIT_B <= 7; CARRY <= 0 when SUM < BASE else 1; end EXAMPLE ;
Declarative part:
  data types
  constants
  intermediate signals
  component declarations
  ...
Statement part (after 'begin'):
  signal assignments
  processes
  component instantiations
  concurrent statements: order not important
   Simulator recalculates sum any time an operand changes
Port is a kind of signal.

## Slide 22: Entity Port Modes
in:
  signal values are read-only
out:
  signal values are write-only
  multiple drivers
buffer:
  similar to out
  signal values may be read from inside
  only 1 driver
inout:
  bidirectional port
Output port modes have to match.

## Slide 23: Use of VHDL Objects

## Slide 24: Structural Model
  توصيف ساختاري functionality را صريحاً توصيف نمي كند بلكه فقط ليستي از اجزا و نحوة اتصال آنهاست.

## Slide 25: Component Declaration
entity FULLADDER is port (A,B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HALFADDER port (X, Y : in bit; SUM, CARRY : out bit); end component;
component ORGATE port (X, Y : in bit; RES : out bit); end component;
signal W_SUM, W_CARRY1, W_CARRY2 : bit;
begin
. . .
In declarative part of architecture
Can use any name for the components
  but better to use the same as entity name
entity HALFADDER is port( X, Y: in bit; SUM, CARRY: out bit); end entity HALFADDER;
entity ORGATE is port( X, Y: in bit; RES: out bit); end entity ORGATE;

## Slide 26: Component Instantiation
architecture STRUCT of FULLADDER is component HALFADDER port (X, Y : in bit; SUM, CARRY : out bit); end component; component ORGATE port (X, Y : in bit; RES : out bit); end component; signal W_SUM, W_CARRY1, W_CARRY2: bit; begin MODULE1: HALFADDER port map( A, B, W_SUM, W_CARRY1 ); MODULE2: HALFADDER port map ( W_SUM, CARRY_IN, SUM, W_CARRY2 ); MODULE3: ORGATE port map ( W_CARRY2, W_CARRY1, CARRY );
end STRUCT;
May need many of each
Instantiation in statement part of architecture (after 'begin')
Wires signals together:
  default: positional association
X
Y
X
Y
SUM
CARRY
SUM
CARRY
X
Y
RES

## Slide 27: Named Signal Association
entity FULLADDER is port (A,B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HALFADDER port (X, Y : in bit; SUM, CARRY : out bit); end component; . . . signal W_SUM, W_CARRY1, W_CARRY2 : bit; begin MODULE1: HALFADDER port map ( X => A, SUM => W_SUM, Y => B, CARRY => W_CARRY1 ); . . . end STRUCT;
Named association:
  left side: "formals" (port names from component declaration)
  right side: "actuals" (architecture signals)
Independent of order in component declaration
X
Y
X
Y
SUM
CARRY
SUM
CARRY
X
Y
RES

## Slide 28: توصیف ساختاری
ساختاری (structural):
⋮
begin
FA1:FULL_ADDER port map (C0, A0, B0, S0, C1);
FA2:FULL_ADDER port map (C1, A1, B1, S1, C2);
FA3:FULL_ADDER port map (C2, A2, B2, S2, C3);
FA4:FULL_ADDER port map (C3, A3, B3, S3, C4);
end;
⋮

## Slide 29: Configuration
architecture … component HA port(X, Y: in bit; SUM, CARRY: out bit); end HALFADDER; signal W_SUM, W_CARRY1, W_CARRY2: bit; begin
· · · MODULE1 : HA port map(A, B, W_SUM, W_CARRY1);
MODULE2: HA port map ( W_SUM, CARRY_IN, SUM, W_CARRY2 );
Entities may be instantiated directly without preceding component declaration
(Not recommended)
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
entity ORGATE is port( A, B: in bit; RES: out bit); end entity ORGATE;
architecture RTL of HALFADDER is begin
…
end architecture RTL;
architecture RTL of ORGATE is begin
…
end architecture RTL;
Library (work)
for MODULE1: HA use entity work.HALFADDER (RTL);
for MODULE2: HA use entity work.HALFADDER (RTL);

## Slide 30: Configuration
Selects entity/architecture pairs for instantiated components
Generates the hierarchy
Default binding rules:
  selects entity with the same name as component
  last compiled architecture is used

## Slide 31: Simple Configuration Specification
entity FULLADDER is port(A, B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HA port(A, B: in bit; SUM, CARRY: out bit); end component;
for MODULE1:HA
use entity work.HALFADDER (RTL);
for MODULE2:HA
use entity work.HALFADDER (GATE);
signal W_SUM, W_CARRY1, W_CARRY2: bit; begin MODULE1:HA port map (…, …); MODULE2:HA port map(…, …);
end STRUCT;
entity HALFADDER is
port(A,B: in bit; S, CY: out bit); end A;
architecture RTL of HALFADDER is · · ·
end RTL;
architecture GATE of HALFADDER is · · ·
end GATE;
Library (work)

## Slide 32: Configuration Declaration
configuration CFG_FULLADDER of FULLADDER is for STRUCT for MODULE2:HA use entity work.HALFADDER(GATE); end for; for others:HA use entity work.HALFADDER(RTL); end for; end for; end CFG_FULLADDER;
Entity/architecture pairs may be selected by use of
  instance names
  'all': all instances of the specified component
  'others': all instances not explicitly mentioned
Possible to reference an existing configuration of a submodule
configuration CONFNAME of ENTITYNAME is
for ARCHNAME
for INSTANCENAME use entity LIBNAME.ENTNAME(ARNAME);
for all:FA use configuration work.CFG_FULLADDER;

## Slide 33: Configuration Declaration

## Slide 34: Configuration
سنتز:
  ابزارهای امروزی پشتیبانی می‌کنند
  بعضي از ابزارهاي سنتز جملات configuration را در نظر نمي‌گيرند و ممکن است قوانين پيش فرض را اعمال کنند.
    در این ابزارها در declarationها:
      نام componentها عين نام entity باشد.
      نام، مود و نوع portها عين پورت entity باشد.