## Slide 1: بهینه‌سازی سرعت

## Slide 2: بهینه سازی سرعت در توصیف
مزایای بهینه سازی سرعت در کد RTL:
  استفاده از پودمان بهینه سازی شده در جای دیگر
  زمان کوتاه تر اجرای ابزارها
  آسیب ندیدن با ارتقای ابزار به نسخة جدید

## Slide 3: روش های بهینه سازی
روش های بهینه سازی در کد RTL
  کدنویسی با توجه به رفتار ابزار (نتیجة سنتز)
  Pipelining (خط لوله گذاری)
  Retiming (باززمانبندی)
  Proper partitioning

## Slide 4: کدنویسی با توجه به رفتار ابزار
  If-then-else تودرتو:
    انتخاب مناسب سیگنال ها با توجه به زمان رسیدنشان
if (X > 7) then ZOUT <= A ; elsif (Y > 13) then ZOUT <= B ; else ZOUT <= C ; end if ;
A
B
C
ZOUT
>
Y
13
>
X
7

## Slide 5: کدنویسی با توجه به رفتار ابزار
  برای شرط های پوشا، case: n:1 MUX  سریع تر
case X is when 0 to 12 => ZOUT <= B ; when 13 => ZOUT <= C ; when others => OUT <= A ; end case ;
if (X > 13) then ZOUT <= A ; elsif (X < 13) then ZOUT <= B ; else ZOUT <= C ; end if ;
A
B
C
<
X
13
>
X
13
ZOUT
<
X
13
>
X
13
=
X
13
A
B
C
ZOUT

## Slide 6: کدنویسی با توجه به رفتار ابزار
  انتخاب مناسب کدهای حالت در FSM
    طراحی به صورت مدودف
       آماده شدن خروجی تقریبا همزمان با تغییر حالت
    کد one-hot
      مدارهای ترکیبی کوچک  تأخیر بین FFها: کم  فرکانس کلاک بالاتر
type STATE_T is (STATE0, STATE1, STATE2, STATE3);
signal STATE, NEXT_STATE : STATE_T;
attribute fsm_encoding : string;
attribute fsm_encoding of STATE : signal is "one-hot";

## Slide 7: Pipelining
Datapath Operation
Inputs
outputs
Registers
Registers
tp= x
Part 1
Inputs
outputs
Registers
Registers
Part 2
Registers
Part 3
Registers
tp= x/3
tp= x/3
tp= x/3
ايدة اصلي:
  عمليات datapath بزرگي را که در يک سيکل ساعت انجام مي شود به چند عمل کوچک که در چند سيکل انجام مي شوند تقسيم کنيم:

## Slide 8: Pipelining
تحلیل زمانی:
  f سه برابر مي شود
    دقیقاً سه برابر؟
  Throughput سه برابر مي شود اما خروجي ها سه کلاک ديرتر حاضر مي شوند:
    Latency:
      Number of clock cycles from the first valid input till the corresponding result available on the output of the pipeline.
    Throughput:
      A measure of how often the pipeline produces the valid output.

## Slide 9: Pipelining
هزينة افزودن رجيسترها:
  بيشتر FPGAها مشکلي ندارند اما در CPLDها pipeline کمتر به کار مي رود.
  CPLDها در يک سطح از آرایة منطقی ترکیبی، عمليات زيادي را مي توانند انجام دهند

## Slide 10: A Systolic FFT Architecture for Real Time FPGA Systems
Preston Jackson, Cy Chan, Charles Rader,
Jonathan Scalera, and Michael Vai
HPEC
ANIMATION EXAMPLE, taken from:
Notes: 1
1

## Slide 11: Example: Baseline Parallel Architecture
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Notes: This is the parallel FFT architecture. When compared with a direct implementation of the DFT, it removes redundant calculations.

## Slide 12: Parallel-Pipelined Architecture
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Notes: The parallel implementation is easily pipelined. This architecture would be 100% efficient if it could be supplied with enough data. However, the number of input pins needed to keep an 8192-point FFT would be 65606, with only 8-bit inputs. Also, A/D converters cannot keep up with this rate of data generation. Thus, a serial design is often used to match with the serial input.

## Slide 13
begin
--
LMULT:MULTIPLIER port map(AR, BR, M1);
LADD:ADDER port map(M1, CR, M2);
LCOMP:COMPARATOR port map(M2, DR, M3);
--
process(CLK)
begin
if rising_edge(CLK) then
if RESET = '1' then
AR <= (others => '0');
BR <= (others => '0');
CR <= (others => '0');
DR <= (others => '0');
ZR <= '0';
else
AR <= A;
BR <= B;
CR <= C;
DR <= D;
ZR <= M3;
end if;
end if;
end process;
--
end ARCH;
entity COMPUTE is
port(CLK: in std_logic;
RESET: in std_logic;
A, B, C, D: in std_logic_vector;
Z: out std_logic);
end COMPUTE;
architecture ARCH of COMPUTE is
signal AR, BR, CR, DR, M1, M2: std_logic_vector (31 downto 0);
signal M3: std_logic;
component MULTIPLIER
port (X, Y: in std_logic_vector;
Z: out std_logic_vector);
end component;
component ADDER
port (X, Y: in std_logic_vector;
Z: out std_logic_vector);
end component;
component COMPARATOR
port (X, Y: in std_logic_vector;
Z: out std_logic);
end component;
begin

## Slide 14
architecture ARCH of COMPUTE is
...
signal M1R, M2R: std_logic_vector (31 downto 0);
begin
--
LMULT:MULTIPLIER port map(AR, BR, M1);
LADD:ADDER port map(M1R, CR, M2);
LCOMP:COMPARATOR port map(M2R, DR, M3);
--
process(CLK)
begin
if rising_edge(CLK) then
if RESET = '1' then
AR <= (others => '0');
BR <= (others => '0');
CR <= (others => '0');
DR <= (others => '0');
ZR <= '0';
M1R <= (others => '0');
M2R <= (others => '0');
else
AR <= A;
BR <= B;
CR <= C;
DR <= D;
ZR <= M3;
M1R <= M1;
M2R <= M2;
end if;
end if;
end process;
--
end arch1;

## Slide 16: Example: AMD AM2901
src_op

## Slide 17: AMD AM2901
library ieee;
use ieee.std_logic_1164.all;
use work.numeric_std.all;
use work.am2901_comps.all;
entity am2901 is port(
clk, rst: in std_logic;
a, b: in unsigned(3 downto 0); -- address inputs
d: in unsigned(3 downto 0); -- direct data
i: in std_logic_vector(8 downto 0); -- micro instruction
c_n: in std_logic; -- carry in
oe: in std_logic; -- output enable
ram0, ram3: inout std_logic; -- shift lines to ram
qs0, qs3: inout std_logic; -- shift lines to q
y: buffer unsigned(3 downto 0); -- data outputs (3-state)
g_bar,p_bar:buffer std_logic; -- carry generate, propagate
ovr: buffer std_logic; -- overflow
c_n4: buffer std_logic; -- carry out
f_0: buffer std_logic; -- f = 0
f3: buffer std_logic); -- f(3) w/o 3-state
end am2901;

## Slide 18
architecture am2901 of am2901 is
alias dest_ctl: std_logic_vector(2 downto 0) is i(8 downto 6);
alias alu_ctl: std_logic_vector(2 downto 0) is i(5 downto 3);
alias src_ctl: std_logic_vector(2 downto 0) is i(2 downto 0);
signal ad, bd: unsigned(3 downto 0);
signal q: unsigned(3 downto 0);
signal r, s: unsigned(3 downto 0);
signal alu_out: unsigned(3 downto 0);
begin
-- instantiate and connect components
u1: ram_regs port map(clk => clk, rst => rst, a => a, b => b, alu_out => alu_out,
dest_ctl => dest_ctl, ram0 => ram0, ram3 => ram3,
ad => ad, bd => bd);
u2: q_reg port map(clk => clk, rst => rst, alu_out => alu_out, dest_ctl => dest_ctl,
qs0 => qs0, qs3 => qs3, q => q);
u3: src_op port map(d => d, ad => ad, bd => bd, q => q,
src_ctl => src_ctl, r => r, s => s);
u4: alu port map(r => r, s => s, c_n => c_n, alu_ctl => alu_ctl,
alu_out => alu_out, g_bar => g_bar, p_bar => p_bar,
c_n4 => c_n4, ovr => ovr);
u5: out_mux port map(ad => ad, alu_out => alu_out, dest_ctl => dest_ctl,
oe => oe, y => y);
-- define f_0 and f3 outputs
f_0 <= '0' when alu_out = "0000" else 'Z';
f3 <= alu_out(3);
end am2901;

## Slide 19: Pipelined AM2901
src_op
براي هماهنگي زماني خروجي ها

## Slide 20: Pipelined AMD AM2901
library ieee;
use ieee.std_logic_1164.all;
use work.numeric_std.all;
use work.am2901_comps.all;
entity am2901 is port(
clk, rst: in std_logic;
a, b: in unsigned(3 downto 0); -- address inputs
d: in unsigned(3 downto 0); -- direct data
i: in std_logic_vector(8 downto 0); -- micro instruction
c_n: in std_logic; -- carry in
oe: in std_logic; -- output enable
ram0, ram3: inout std_logic; -- shift lines to ram
qs0, qs3: inout std_logic; -- shift lines to q
y: buffer unsigned(3 downto 0); -- data outputs (3-state)
g_bar_q,p_bar_q:buffer std_logic; -- carry generate, propagate
ovr_q: buffer std_logic; -- overflow
c_n4_q: buffer std_logic; -- carry out
f_0: buffer std_logic; -- alu_out = 0
f3: buffer std_logic); -- alu_out(3) w/o 3-state
end am2901;

## Slide 21
architecture am2901 of am2901 is
alias dest_ctl: std_logic_vector(2 downto 0) is i(8 downto 6);
alias alu_ctl: std_logic_vector(2 downto 0) is i(5 downto 3);
alias src_ctl: std_logic_vector(2 downto 0) is i(2 downto 0);
signal ad, bd: unsigned(3 downto 0);
signal q: unsigned(3 downto 0);
signal r, s: unsigned(3 downto 0);
signal alu_out, alu_out_q: unsigned(3 downto 0);
begin
-- instantiate and connect components
u1: ram_regs port map(clk => clk, rst => rst, a => a, b => b, alu_out => alu_out_q,
dest_ctl => dest_ctl, ram0 => ram0, ram3 => ram3,
ad => ad, bd => bd);
u2: q_reg port map(clk => clk, rst => rst, alu_out => alu_out _q, dest_ctl => dest_ctl,
qs0 => qs0, qs3 => qs3, q => q);
u3: src_op port map(d => d, ad => ad, bd => bd, q => q,
src_ctl => src_ctl, r => r, s => s);
u4: alu port map(r => r, s => s, c_n => c_n, alu_ctl => alu_ctl,
alu_out => alu_out, g_bar => g_bar, p_bar => p_bar,
c_n4 => c_n4, ovr => ovr);
u5: out_mux port map(ad => ad, alu_out => alu_out _q, dest_ctl => dest_ctl,
oe => oe, y => y);
-- define f_0 and f3 outputs
f_0 <= '0' when alu_out _q = "0000" else 'Z';
f3 <= alu_out _q(3);
No change

## Slide 22: Pipelined AMD AM2901
process (clk)
if (rising_edge(clk) then
alu_out_q <= alu_out;
g_bar_q <= g_bar;
p_bar_q <= p_bar;
ovr_q <= ovr;
c_n4_q <= c_n4;
end if;
end process;
end am2901;

## Slide 23: بهینه سازی در کد VHDL
مشخص کردن ساختار با پرانتر:
  تأخیر مسیر بحرانی در ساختار درختی متعادل

## Slide 24: بهینه سازی در کد VHDL
مشخص کردن ساختار با پرانتر:
  اگر ورودی ای دیرتر برسد:
    برای ورودی IN2 انتخاب شود
(?)

## Slide 25: Retiming (باززمانبندی)
هدف اصلی:
  افزایش فرکانس کلاک مدار ترتیبی
اهداف فرعی:
  کاهش مساحت
  کاهش توان مصرفی

## Slide 26: Retiming
تعریف:
  جابجایی FFها در مدار برای بهبود کارایی بدون تغییر latency

## Slide 27: Retiming
  جابجایی FFها در مدار ترکیبی بدون تغییر تعداد آنها
    در یک مسیر از Piها تا Poها
    در یک حلقه
     latency ورودی/خروجی تغییر نمی کند
    رفتار مدار تغییر نمی کند

## Slide 28: Retiming
  عدم تغییر در اندازة مدار ترکیبی
  امکان تغییر در اندازة بخش FFها
    سربار مساحت
    گاهی با هدف حداقل کردن تعداد FFها

## Slide 29: Retiming
  در FPGA

## Slide 30: Retiming
تأثیر در FSM:
  تغییر کد حالت:
    خراب شدن کدهای مدودف
    خراب شدن کدهای بامعنا (کد حالت اولیه)
  مثال:
    می خواهیم FF A و FF B در حالت اولیه مخالف باشند.
       نیاز به اعمال محدودیت اضافه